## Slide 1
Datacenter Modernization from Hyper-V to Hyper-Converged Infrastructure
Elden Christensen
EldenC@Microsoft.Com
Principal PM Manager

## Slide 2
Hyper-Converged Infrastructure Market Opportunity
Storage Spaces Direct 10 Ways It’s Better in WS 2019
Software Defined Networking Network Controller and Gateway
RDMA
Cluster Sets Scaling Out
Agenda

## Slide 3
IDC Worldwide Quarterly Converged Systems Tracker, Q1 2017
https://thestack.com/data-centre/2017/06/26/hyperconverged-market-grows-64-over-2016/
In 2017
+65%
HCI Adoption YoY
Gartner Press Release
https://www.gartner.com/newsroom/id/3308017
By 2019
$5B
Market Size

## Slide 4
Worldwide adoption of Storage Spaces Direct
clusters in 18 months since general availability

## Slide 5
Standard x86 servers
+
Local drives
+
The magic of software
Hyper-Converged Infrastructure (HCI)
Legacy “Three Tier” Infrastructure
Hypervisors
Storage (SAN)
Storage Fabric
Ethernet Switches
Misc. Appliances
Ethernet Switches

## Slide 6
Standard x86 servers
+
Local drives
+
The magic of software
Hyper-Converged Infrastructure (HCI)
Legacy “Three Tier” Infrastructure
Hypervisors
Storage (SAN)
Storage Fabric
Ethernet Switches
Misc. Appliances
Ethernet Switches

## Slide 7
Hyper-V
Storage Spaces Direct
Introduced in 2008, ten years ago!
Foundation of our hyperscale Azure cloud
New in Windows Server 2016
In development for 5+ years at Microsoft
Foundation of Azure Stack
SDN
New in Windows Server 2016
Taken directly from Azure

## Slide 8
Two options to procure, both supported
Build Your Own
1
2
Partner Solutions

## Slide 9: Learn more at microsoft.com/wssd

## Slide 10
Why is Windows Server better than [competitor] ?

## Slide 11
Lower costs
No proprietary hardware or vendor lock-in
Choice of industry-standard servers and components
Reduce datacenter footprint and power and cooling cost
Hyper-converged infrastructure has many advantages
Unified management
End-to-end visibility across the whole stack
Consistent, unified experience across compute, networking, storage
Reduce Op Ex
Innovate faster
100x more servers sold every year than storage arrays
Inflection point in hardware, from NVMe to RDMA
Innovations come to Windows Server first
Single vendor
Single source for procurement and support
Pre-validated, no integration work
With Windows, no separate licenses, and included guests!
Simple scalability and expansion
Buy what you need today, reduce Cap Ex
Scale by adding servers, one by one
Cloud-inspired architecture enables near-limitless scale
Built-in balancing makes planning easy

## Slide 12
Unified management
End-to-end visibility across the whole stack
Consistent, unified experience across compute, networking, storage
Reduce Op Ex
Innovate faster
100x more servers sold every year than storage arrays
Inflection point in hardware, from NVMe to RDMA
Innovations come to Windows Server first
Single vendor
Single source for procurement and support
Pre-validated, no integration work
With Windows, no separate licenses, and included guests!
Simple scalability and expansion
Buy what you need today, reduce Cap Ex
Scale by adding servers, one by one
Cloud-inspired architecture enables near-limitless scale
Built-in balancing makes planning easy
Lower costs
No proprietary hardware or vendor lock-in
Choice of industry-standard servers and components
Reduce datacenter footprint and power and cooling cost
Advantages of Hyper-Converged Infrastructure on Windows

## Slide 13
Included in Windows Server Datacenter
Hypervisor / compute
Software-defined storage
Software-defined networking
Management software
Unlimited guest licenses
Source: https://www.microsoft.com/en-us/cloud-platform/windows-server-pricing

## Slide 14
Unified management
End-to-end visibility across the whole stack
Consistent, unified experience across compute, networking, storage
Reduce Op Ex
Innovate faster
100x more servers sold every year than storage arrays
Inflection point in hardware, from NVMe to RDMA
Innovations come to Windows Server first
Single vendor
Single source for procurement and support
Pre-validated, no integration work
With Windows, no separate licenses, and included guests!
Simple scalability and expansion
Buy what you need today, reduce Cap Ex
Scale by adding servers, one by one
Cloud-inspired architecture enables near-limitless scale
Built-in balancing makes planning easy
Lower costs
No proprietary hardware or vendor lock-in
Choice of industry-standard servers and components
Reduce datacenter footprint and power and cooling cost
Advantages of Hyper-Converged Infrastructure on Windows

## Slide 15
Unified management
End-to-end visibility across the whole stack
Consistent, unified experience across compute, networking, storage
Reduce Op Ex
Single vendor
Single source for procurement and support
Pre-validated, no integration work
With Windows, no separate licenses, and included guests!
Simple scalability and expansion
Buy what you need today, reduce Cap Ex
Scale by adding servers, one by one
Cloud-inspired architecture enables near-limitless scale
Built-in balancing makes planning easy
Lower costs
No proprietary hardware or vendor lock-in
Choice of industry-standard servers and components
Reduce datacenter footprint and power and cooling cost
Innovate faster
100x more servers sold every year than storage arrays
Inflection point in hardware, from NVMe to RDMA
Innovations come to Windows Server first
Advantages of Hyper-Converged Infrastructure on Windows

## Slide 16
Windows Server HCI is on the leading edge
Persistent memory
Intel Xeon® Scalable®
3D XPoint
Intel Thunderbolt™ 3
Available to Windows Insiders,
in Windows Server 2019
Supported since announcement on Windows Server 2016
Supported since announcement on Windows Server 2016
Blazing the trail for switchless networking
of x86 hardware innovation
OPTANE™
NVMe
Fully supported M.2, U.2, Add-In-Card (AIC)
RDMA
Unique to Windows software-defined storage

## Slide 17
Unified management
End-to-end visibility across the whole stack
Consistent, unified experience across compute, networking, storage
Reduce Op Ex
Innovate faster
100x more servers sold every year than storage arrays
Inflection point in hardware, from NVMe to RDMA
Innovations come to Windows Server first
Single vendor
Single source for procurement and support
Pre-validated, no integration work
With Windows, no separate licenses, and included guests!
Simple scalability and expansion
Buy what you need today, reduce Cap Ex
Scale by adding servers, one by one
Cloud-inspired architecture enables near-limitless scale
Built-in balancing makes planning easy
Lower costs
No proprietary hardware or vendor lock-in
Choice of industry-standard servers and components
Reduce datacenter footprint and power and cooling cost
Advantages of Hyper-Converged Infrastructure on Windows

## Slide 18
Innovate faster
100x more servers sold every year than storage arrays
Inflection point in hardware, from NVMe to RDMA
Innovations come to Windows Server first
Single vendor
Single source for procurement and support
Pre-validated, no integration work
With Windows, no separate licenses, and included guests!
Simple scalability and expansion
Buy what you need today, reduce Cap Ex
Scale by adding servers, one by one
Cloud-inspired architecture enables near-limitless scale
Built-in balancing makes planning easy
Lower costs
No proprietary hardware or vendor lock-in
Choice of industry-standard servers and components
Reduce datacenter footprint and power and cooling cost
Advantages of Hyper-Converged Infrastructure on Windows
Unified management
End-to-end visibility across the whole stack
Consistent, unified experience across compute, networking, storage
Reduce Op Ex

## Slide 19
Windows Admin Center
announced at Microsoft Ignite 2017

## Slide 20
Install project 'Honolulu’ in under 2 minutes
New dashboard for Hyper-Converged Infrastructure
Hyper-V management
Storage Spaces management
Create virtual machine
Alerts and tolerating multiple failures
Storage class memory teaser
Scale out with self-balancing compute and storage
Deduplication and compression
Prepare for the worst with Azure Site Recovery

## Slide 21
Watch the recording
Manage and monitor your Windows Server 2016 hyper-converged infrastructure - BRK3123
youtube.com/watch?v=CkZgq5RuJHs&

## Slide 22: FAQs – Windows Admin Center for HCI
Q: How long does it take to download and install?
A: Under 5 minutes.
Q: Does it cost money?
A: No.
Q: Does it require System Center?
A: No.
Q: Does it require an Internet connection?
A: No.

## Slide 23: aka.ms/StorageSpacesDirect > Manage in Windows Admin Center

## Slide 24
Windows Server offers the fastest, most affordable, and (soon) most easily managed path to Hyper-Converged Infrastructure.

## Slide 25
Hyper-Converged Infrastructure Market Opportunity
Storage Spaces Direct 10 Ways It’s Better in WS 2019
Software Defined Networking Network Controller and Gateway
RDMA
Cluster Sets Scaling Out
Agenda

## Slide 26
– 1 –
Relaxed hardware requirements

## Slide 27: Hardware requirements
Windows Server
2016
Windows Server
2019
Applies to both versions
Less endurance
Recommended 3+ DWPD or 4+ TBW for cache drives
DWPD
& TBW
Less cache
As low as 5% at large scale or with very high endurance
Mix-and-match
Drives of different models and sizes for replacement or expansion

## Slide 28: aka.ms/StorageSpacesDirect > Hardware Requirements

## Slide 29
– 2 –
For two-node…

## Slide 30
Two servers
Full-featured, cost-effective, surprisingly popular

## Slide 31: Quorum without another server or virtual machine, without Internet, and even without Active Directory, for under $5.
introducing TRUE TWO-NODE
USB

## Slide 32: Quorum without another server or virtual machine, without Internet, and even without Active Directory, for under $5.
introducing TRUE TWO-NODE
USB

## Slide 33: Quorum without another server or virtual machine, without Internet, and even without Active Directory, for under $5.
Windows Server
2019
Applies only to
USB
introducing TRUE TWO-NODE

## Slide 34
* Image courtesy of Linksys
USB
Router
Server #2
Server #1
Uplink
1 GbE
10 GbE
Switchless
10 GbE
10 GbE
How it works

## Slide 35
1
Plug in USB
Insert the USB storage device into the port on the router
2
Share from router
In the router’s UI, set the share name, username, and password for access
Use as witness
3
New parameter to provide credentials to Windows for safekeeping
Set-ClusterQuorum
-FileShareWitness \\Server\Share
-Credential $(Get-Credential)
Simple set-up experience

## Slide 36
USB
Router
Server #2
Server #1
Uplink
1 GbE
10 GbE
Switchless
10 GbE
10 GbE
How it works

## Slide 37: NEW! USB Witness
Windows Server
2019
Applies only to
Extremely low cost
  Router
    Needed anyway for uplink
    Use any router from any major vendor
    Need USB and SMB 2+ support
  USB storage device
    Any size, witness.log is under 1 KB
    Pack of 10 for $20 online
Works anywhere
  Without
    Any other server, unlike File Share Witness
    Internet, unlike Cloud Witness
    Active Directory
  Rugged
    Minimal power footprint
    No moving parts
Available today in Insider Preview

## Slide 38
– 3 –
Nested resiliency

## Slide 39
“RAID-51 is the RAID level for the truly paranoid, the "belt and suspenders" technique to maximize fault tolerance and availability, at the expense of just about everything else.”
- PC Guide
Server 1
Server 2
RAID-1 (Two-Way Mirror)
Between Servers
Data
“A”
Data
“B”
Data
“C”
Data
“D”
Data
“E”
Parity
P1
RAID-5 (Single Parity) Within Server
Copy
“A”
Copy
“B”
Copy
“C”
Copy
“D”
Copy
“E”
Copy
P1
RAID-5 (Single Parity) Within Server

## Slide 40: Nested two-way mirror Effectively, You have four copies
100% Mirror
Server 1
Server 2
Volume
Data
Copy
Copy
Copy
Two-Way Mirror at
StorageScaleUnit level
Two-Way Mirror at
PhysicalDisk level
Two-Way Mirror at
PhysicalDisk level
LBA 0, 1, 2, 3…
...N

## Slide 41: Nested mirror- accelerated parity Effectively, Option 1 + RAID-51
Parity
Mirror
Server 1
Server 2
Volume
LBA 0, 1, 2, 3…
...N
Writes
Data
Copy
Copy
Copy
Two-Way Mirror
Node-local
single parity
Node-local
two-way mirror
Data
Data
Data
P1
Copy
Copy
Copy
P1

## Slide 42: Survive simultaneous failures with just 2 nodes
Stays online
When 1 server and 1 capacity drive are lost,
Server 1
Server 2
Stays online
When any 2 capacity drives are lost,
Server 1
Server 2
When 1 server and 1 cache drive are lost,
Server 1
Server 2
Stays online*
* Upon first failure, the cache will switch to read-only (not read/write) and must drain prior to the second failure

## Slide 43: How much usable space do I get?
~50%
Normal two-way mirror
~33%
Normal three-way mirror*
~25%
Nested two-way mirror
New!
~40%
Nested mirror-accelerated parity**
New!
* Requires three nodes ** Depends on the number of capacity drives – more is better, up to 8

## Slide 44
– 4 –
Deduplication and compression

## Slide 45: Together at last
Resilient File System
  Recommend for Storage Spaces
    Detect and correct corruptions
    Mirror-accelerated parity
  Great features for Hyper-V
    Faster VHDX creation / expansion
    VHDX checkpoint integration
  Learn more at aka.ms/refs
Data Deduplication
  Highly optimized
    Outside of IO path (post-processing)
    Variable-size chunk store
    Multi-threaded
  Highly scalable
    Volumes up to 64 TB
    Files up to 1 TB
  Learn more at aka.ms/dedup
Available today in Insider Preview
Windows Server
2019
Applies only to

## Slide 46: Turn on with one click
Windows Server
2019
Applies only to

## Slide 47: Get up to 10X more usable storage for free!
30%
Savings
60%
Savings
90%
Savings
Virtual hard disk files, .iso files, backup
General-purpose file server
Documents, photos, music, videos

## Slide 48
– 5 –
Scale up, up, and away!

## Slide 49
1 petabyte (PB) = 1,000 terabytes (TB)
Max scale?

## Slide 50
1 petabyte (PB) = 1,000 terabytes (TB)
1 PB
Windows Server 2016

## Slide 51
1 PB
Windows Server 2016
1 petabyte (PB) = 1,000 terabytes (TB)
4 PB
Windows Server 2019

## Slide 52: NEW! Larger maximum scale
Limit / Recommendation | Windows Server 2016 | Windows Server 2019 | Increase
Max servers per cluster | 16 | 16 | -
Max drives per cluster | 416 | 416 | -
Max raw capacity per cluster | 1 PB | 4 PB | 4x
Max raw capacity per server | 100 TB | 400 TB | 4x
Max number of volumes | 32 | 64 | 2x
Max size per volume | 32 TB | 64 TB | 2x
Windows Server
2019
Applies only to

## Slide 53
– 6 –
Persistent memory

## Slide 54: Types of drives
Non-Volatile Memory Express
Connected via PCIe, includes M.2, U.2, Add-In-Card, and Intel Optane (3D X-Point)
Solid-State Drive
Any SSD connected via SATA or SAS, must have power-loss protection (PLP)
Hard Disk Drive
Any HDD connected via SATA or SAS, can be any RPM
Persistent Memory
NVDIMM-N, Intel Optane DIMMs
PMEM

## Slide 55: Types of drives
Non-Volatile Memory Express
Connected via PCIe, includes M.2, U.2, Add-In-Card, and Intel Optane (3D X-Point)
Solid-State Drive
Any SSD connected via SATA or SAS, must have power-loss protection (PLP)
Hard Disk Drive
Any HDD connected via SATA or SAS, can be any RPM
Persistent Memory
NVDIMM-N, Intel Optane DIMMs
PMEM
~ 10 ms
10,000,000 ns
~ 5 µs
5,000 ns
~ 0.1 ms
100,000 ns
~ 0.1 ms
100,000 ns

## Slide 56: Types of drives
PMEM
~ 10 ms
10,000,000 ns
~ 10 µs
5,000 ns
~ 0.1 ms
100,000 ns
~ 0.1 ms
100,000 ns

## Slide 57: Persistent memory
* Image courtesy of Intel

## Slide 58: Persistent memory
Full support with Storage Spaces Direct
  Use as cache
    Accelerate active working set
  Use as capacity
    Extremely consistent, low latency
Simple and familiar user experience
  “Just another physical disk”
    With new MediaType
  Use PowerShell or Windows Admin Center
Windows Server
2019
Applies only to
* Image courtesy of Intel

## Slide 59
– 7 –
Faster mirror-accelerated parity

## Slide 60: Mirror-accelerated parity
Create volume that’s part mirror, part parity
  Write to mirror, “rotate” to parity later
  Defer compute-intensive calculation to nearline
Strike the right balance
  You choose the ratio of mirror-to-parity
  Tradeoff performance for storage efficiency
Windows Server
2016
Windows Server
2019
Applies to both versions

## Slide 61: Mirror-accelerated parity gives capacity back
Mirror/Parity Ratio | Mirror Overhead | Parity Overhead | Example Size | Example Footprint
100% mirror | 3x | 2x (RS 2+2) | 10 TB | 30 TB
30% mirror, 70% parity | 3x | 2x (RS 2+2) | 10 TB | 23 TB
20% mirror, 80% parity | 3x | 2x (RS 2+2) | 10 TB | 22 TB
10% mirror, 90% parity | 3x | 2x (RS 2+2) | 10 TB | 21 TB
4 nodes
Mirror/Parity Ratio | Mirror Overhead | Parity Overhead | Example Size | Example Footprint
100% mirror | 3x | 1.5x (RS 4+2) | 10 TB | 30 TB
30% mirror, 70% parity | 3x | 1.5x (RS 4+2) | 10 TB | 19.5 TB
20% mirror, 80% parity | 3x | 1.5x (RS 4+2) | 10 TB | 18 TB
10% mirror, 90% parity | 3x | 1.5x (RS 4+2) | 10 TB | 16.5 TB
8 nodes
Mirror/Parity Ratio | Mirror Overhead | Parity Overhead | Example Size | Example Footprint
100% mirror | 3x | 1.375x (LRC 8,2,1) | 10 TB | 30 TB
30% mirror, 70% parity | 3x | 1.375x (LRC 8,2,1) | 10 TB | 18.625 TB
20% mirror, 80% parity | 3x | 1.375x (LRC 8,2,1) | 10 TB | 17 TB
10% mirror, 90% parity | 3x | 1.375x (LRC 8,2,1) | 10 TB | 15.375 TB
12 nodes
2x

## Slide 62
Measured with 4K random IO, drifting working set, and 70/30 read/write mix
Baseline
Windows Server 2016

## Slide 63
+100%
Windows Server 2019
Measured with 4K random IO, drifting working set, and 70/30 read/write mix
Baseline
Windows Server 2016

## Slide 64: NEW! 100% Faster mirror-accelerated parity
Capacity efficiency in %
Storage performance in IOPS
* Mirror-accelerated parity outperforms dual parity, especially in Windows Server 2019, but three-way mirror remains the clear performance leader.
* Three-way mirror has 33.3% storage efficiency. Dual parity starts at 50.0% and goes up to 80.0%. Mirror-accelerated parity is in between.
Three-way mirror
Dual parity
Mirror-accelerated parity
Three-way mirror
Dual parity
Mirror-accelerated parity
+100%
Windows Server
2019
Applies only to

## Slide 65
– 8 –
Built-in performance history

## Slide 67
You do not need to install, configure, or start anything. An external database is not required.
An Internet connection is not required.
System Center is not required.

## Slide 68: Were there any CPU spikes last week?

## Slide 69: Were there any CPU spikes last week?

## Slide 70
aka.ms/ClusterPerformanceHistory

## Slide 71
– 9 –
Built-in outlier detection

## Slide 73: NEW! Proactive outlier detection
Continuously monitor drive latency
  Organize drives into peer groups
  Compare every drive’s mean latency against its peers
  Compare every drive’s tail (99th percentile) latency against its peers
Proven in Azure
  Long-standing and very successful approach
Windows Server
2019
Applies only to

## Slide 75
(6) Group A
(5) Group B
(17) Group C
Group by media and usage

## Slide 76
Variety of analyses, including rolling average and tail latency
(6) Group A
(5) Group B
(17) Group C
Latency

## Slide 77
Azure-inspired outlier detection algorithm
(6) Group A
(5) Group B
(17) Group C
Latency

## Slide 78
– 10 –
Simpler PowerShell

## Slide 79
Clear-ClusterNode -CleanUpDisks
Wipe drives to start over
New-Volume -FriendlyName Example -Size 100GB
Provision
Get-SddcDiagnosticInfo
Gather every relevant log

## Slide 80
Get-SddcDiagnosticInfo
Gather every relevant log
https://docs.microsoft.com/en-us/windows-server/storage/storage-spaces/data-collection
Update from PowerShell Gallery or GitHub
Tip: Use Import-Clixml to read xml files:
PS C:\temp\HealthTest> Import-Clixml -Path .\WM_ClusPort.xml | ? deviceattribute -eq 1312 | ft ConnectedNode, DeviceGuid
ConnectedNode DeviceGuid
------------- ----------
YS0009UK {da56b3f8-2e04-60be-2880-76596938d165}
YS0009UK {36aa9ccc-941d-6ca0-6a3b-7ad17dd421a5}
YS0009UK {8cd0801c-f79f-bc29-349b-0dee7232c6ca}

## Slide 81
Relaxed hardware requirements
USB witness for two-node at the edge
Nested resiliency (RAID-51) for two-node
Deduplication and compression
Scale up to 4 PB
Full support for persistent memory
Mirror-accelerated parity is 100% faster
Built-in performance history
Built-in outlier detection
Simpler PowerShell
What’s New
for Storage Spaces Direct

## Slide 82
Learn more at
aka.ms/StorageSpacesDirect

## Slide 83
Learn more at
aka.ms/SpacesDirect

## Slide 84
Learn more at
aka.ms/s2d

## Slide 85: Hands-on-Lab Windows Admin Center

## Slide 86
Hyper-Converged Infrastructure Market Opportunity
Storage Spaces Direct 10 Ways It’s Better in WS 2019
Software Defined Networking Network Controller and Gateway
RDMA
Cluster Sets Scaling Out
Agenda

## Slide 87
Hyper-Converged Infrastructure Market Opportunity
Storage Spaces Direct 10 Ways It’s Better in WS 2019
Software Defined Networking Network Controller and Gateway
RDMA
Cluster Sets Scaling out
Agenda

## Slide 88: Scale AND Resiliency
Cluster 1
Cluster 2
Cluster 4
Cluster 3

## Slide 89: Hyperscale for Hyper-converged
Cluster Set Head
Centralized Cluster Set Management
Unified Namespace \\ClusterSet\Share1
Cluster 1
Cluster 2
Cluster 3
Cluster 4

## Slide 90: Hyperscale for Hyper-converged
Loosely couples a grouping of multiple clusters (think clustering clusters)
Cluster Set Head
Centralized Cluster Set Management
Unified Namespace \\ClusterSet\Share1
Cluster 1
Cluster 2
Cluster 3
Cluster 4

## Slide 91: Hyperscale for Hyper-converged
Loosely couples a grouping of multiple clusters (think clustering clusters)
Increases cluster nodes and storage
Cluster Set Head
Centralized Cluster Set Management
Unified Namespace \\ClusterSet\Share1
Cluster 1
Cluster 2
Cluster 3
Cluster 4

## Slide 92: Hyperscale for Hyper-converged
Loosely couples a grouping of multiple clusters (think clustering clusters)
Increases cluster nodes and storage
Utilizes a self-managed namespace
Cluster Set Head
Centralized Cluster Set Management
Unified Namespace \\ClusterSet\Share1
Cluster 1
Cluster 2
Cluster 3
Cluster 4

## Slide 93: Hyperscale for Hyper-converged
Loosely couples a grouping of multiple clusters (think clustering clusters)
Increases cluster nodes and storage
Utilizes a self-managed namespace
Have your scale and keep your resiliency too
Cluster Set Head
Centralized Cluster Set Management
Unified Namespace \\ClusterSet\Share1
Cluster 1
Cluster 2
Cluster 3
Cluster 4

## Slide 94: What does Cluster Sets do?
Cluster Set Head
Centralized Cluster Set Management
Unified Namespace \\ClusterSet\Share1
Cluster 1
Cluster 2
Cluster 3
Cluster 4

## Slide 95: What does Cluster Sets do?
Allows for virtual machine fluidity
Cluster Set Head
Centralized Cluster Set Management
Unified Namespace \\ClusterSet\Share1
Cluster 1
Cluster 2
Cluster 3
Cluster 4

## Slide 96: What does Cluster Sets do?
Allows for virtual machine fluidity
Places new virtual machines on an optimal node
Cluster Set Head
Centralized Cluster Set Management
Unified Namespace \\ClusterSet\Share1
Cluster 1
Cluster 2
Cluster 3
Cluster 4

## Slide 97: What does Cluster Sets do?
Allows for virtual machine fluidity
Places new virtual machines on an optimal node
Allows movement of the VMs between clusters without changing storage paths
Cluster Set Head
Centralized Cluster Set Management
Unified Namespace \\ClusterSet\Share1
Cluster 1
Cluster 2
Cluster 3
Cluster 4

## Slide 98: What does Cluster Sets do?
Allows for virtual machine fluidity
Places new virtual machines on an optimal node
Allows movement of the VMs between clusters without changing storage paths
Takes advantage of a new role “Infrastructure Scale Out File Server”
Cluster Set Head
Centralized Cluster Set Management
Unified Namespace \\ClusterSet\Share1
Cluster 1
Cluster 2
Cluster 3
Cluster 4

## Slide 99: What does Cluster Sets do?
Allows for virtual machine fluidity
Places new virtual machines on an optimal node
Allows movement of the VMs between clusters without changing storage paths
Takes advantage of a new role “Infrastructure Scale Out File Server”
Takes advantage of the new SMB feature “SMB Loopback”
Cluster Set Head
Centralized Cluster Set Management
Unified Namespace \\ClusterSet\Share1
Cluster 1
Cluster 2
Cluster 3
Cluster 4